## Slide 1: Database of Urban Transport Times
Qualitative comparison and analysis of transport inequality within and between cities.

## Slide 2: Accessibility Inequality
Mobility by car, bike, walking and transit.
Which areas of the city might be less mobile?
  Using population density as a proxy variables for opportunities, more=better
Hypothesis: Areas in city center might be more attractive for cycling

## Slide 3: Lots of Isochrones as a measure
Meaning: Iso (equal) chrone (time)
Polygons of reachable areas by modality using max time.
Here right: isochrones and population density for 3 points

## Slide 4: Cities Queried
Vienna
Graz
Brussels
Berlin
Hamburg
Copenhagen
Aarhus
Paris
Marseille
London
Birmingham
York
Luxembourg
Amsterdam
Utrecht + 5 more Dutch
Stockholm
Gothenburg
Helsinki
Oslo
Warsaw
Barcelona
Madrid
Lisbon
Bern
32 more scheduled..
Sources
  GHS population and urban center grid
    from Global Human Settlement Layer
  GraphHopper:
    driving, walking, cycling & transit
  Bing Maps (academic):
    driving (calibration for Graphhopper)
  * Transit is not reliable enough from either source currently, working on GTFS-based GraphHopper, requires some small fixes.

## Slide 5: For Each City:
Create raster with points
Query Bing for isochrones for car
Create OSM & TransitLand GTFS extracts for Graphhopper
  Generate direction graph in GraphHopper docker
Fetch all records for all modes per city for 5-15-…-55 minutes
Calculate overlapping grids with isochrones
  More than 150.000 isochrones collected (!)
Export as DataPackage

## Slide 6: Graphhopper vs Here Maps (Brussels)
Graphhopper very optimistic with speeds, average speed should be brought down in settings. Requires full refetch!

## Slide 7: Population Access: Amsterdam & Utrecht

## Slide 8: Example results: Amsterdam & Utrecht

## Slide 9: Example results in the Netherlands
A higher score means cycling reaches the same fraction of population as driving in does.
Excluding parking times, which averages more than 5 minutes.

## Slide 10: Example results in Europe
Reachable 0.5 by bike

## Slide 11: Gini Index
Preliminary Examples, lower=better (not corrected for population density
Ideas to compare cities or neighborhoods?

## Slide 12: To-Do Generation
Analysis:
  Average size of 15-minute isochrone
  Average speed
    Time to reach edge of isochrone
    Can represent “Urban Form” factor as well, optimisation for bikes/cars
Generate characteristics from urban layout, more than just density.

## Slide 13: Discussion
No correction of mobility vs population density. Good/bad?
What other methods/numbers can we derive from this?